## Slide 1: DMVPN

## Slide 2: Phase 1
Hub
Spoke
Int tunnel 10
ip mtu 1400
ip tcp adjust-mss 1360
ip address 172.16.1.1 255.255.255.0
tunnel source gi 2
tunnel mode gre multipoint
tunnel-key 1
ip nhrp network-id 1
ip nhrp authentication C1sc0123
ip nhrp multicast map dynamic
Int tunnel 10
ip mtu 1400
ip tcp adjust-mss 1360
ip address 172.16.1.2 255.255.255.0
tunnel source gi 2
tunnel destination 10.1.1.1
tunnel-key 1
ip nhrp network-id 1
ip nhrp authentication C1sc0123
ip nhrp nhs 172.16.1.1
ip nhrp map 172.16.1.1 10.1.1.1
ip nhrp multicast map 10.1.1.1

## Slide 3: Phase 2
Hub
Spoke
Int tunnel 10
ip mtu 1400
ip tcp adjust-mss 1360
ip address 172.16.1.1 255.255.255.0
tunnel source gi 2
tunnel mode gre multipoint
tunnel-key 1
ip nhrp network-id 1
ip nhrp authentication C1sc0123
ip nhrp multicast map dynamic
Int tunnel 10
ip mtu 1400
ip tcp adjust-mss 1360
ip address 172.16.1.2 255.255.255.0
tunnel source gi 2
tunnel mode gre multipoint
tunnel-key 1
ip nhrp network-id 1
ip nhrp authentication C1sc0123
ip nhrp nhs 172.16.1.1
ip nhrp map 172.16.1.1 10.1.1.1
ip nhrp multicast map 10.1.1.1

## Slide 4: Phase 3
Hub
Spoke
Int tunnel 10
ip mtu 1400
ip tcp adjust-mss 1360
ip address 172.16.1.1 255.255.255.0
tunnel source gi 2
tunnel mode gre multipoint
tunnel-key 1
ip nhrp network-id 1
ip nhrp authentication C1sc0123
ip nhrp multicast map dynamic
ip nhrp redirect
Int tunnel 10
ip mtu 1400
ip tcp adjust-mss 1360
ip address 172.16.1.2 255.255.255.0
tunnel source gi 2
tunnel mode gre multipoint
tunnel-key 1
ip nhrp network-id 1
ip nhrp authentication C1sc0123
ip nhrp nhs 172.16.1.1
ip nhrp map 172.16.1.1 10.1.1.1
ip nhrp multicast map 10.1.1.1
ip nhrp shortcut